## Slide 1: Reminder:
Clean values in PEEC_demo and open the good sheet prior to the presentation
Have the report opened + GaBi?

## Slide 2: Developing a Parameterized Embodied Emissions Calculator (PEEC) for telecommunication networks equipment
Master’s thesis presentation
Maël Madon

## Slide 3: Context
Halved by 2030
Net zero by 2050

## Slide 4: Problem
Carbon footprint of ICT = rather new field
  No consensus in research on ICT footprint (around 1-3% annual emissions)
  Few precise environmental assessments of ICT products: even less for telecommunication networks
Challenging CO2 assessments
Questions from customers and citizens
Evolving CO2 reporting practices
CO2
ICT = Information and Communication Technology

## Slide 5: What did I do?
Ericsson Sustainability Research
Focus on
  Telecommunication network equipment
  Embodied emissions
  Usability and simplifications
Embodied emissions
= ”cradle-to-gate” emissions
=> Research question:
  How could embodied emissions of telecommunication networks be estimated in a streamlined way?

## Slide 6: Outcome of the project
Parameterized Embodied Emission Calculator for telecommunication network equipment
=> DEMO <=
PEEC

## Slide 7: Method
Life Cycle Assessment (LCA)
LCA data and tools
User expectations
Workshop on usability
LCA standards
LCA experts
Previous LCA for telecom
Literature on simplified LCA
11 customer requests
Discussion with stakeholders

## Slide 8: Similar work
PAIA (MIT and Quantis)
iNEMI Eco-Impact Estimator

## Slide 9: Limitations
Experimental validation: challenging because no data to test the model against
  Comparison with literature
  Compliance with standards
  Systematic discussion about sources of uncertainties
  Sensitivity analysis
Limited scope
  Environmental indicators
  Life cycle stages included
Limited method to study usability
Quality of the results depend on the quality of data

## Slide 10: Conclusion
PEEC = carbon footprinter for telecom products
Transparent method
Use case for industry
  Report CO2 emissions
  Answer customer questions
  Help research projects

## Slide 11: Future work
Update data for new products
  Material declarations
  Energy consumption in production processes
  Transport in the supply chain
Include other environmental indicator
Include other life cycle stages
Further study the adoption and validity of the tool
Consider collaboration with existing tools

## Slide 12: Thanks for your attention!
Questions and discussion

## Slide 13: Sensitivity analysis
Modified parameter | Description | Motivation
Plastics impact factor | Doubled (from 2,5 to 5) | The figure used for plastics is an estimation. We try a more conservative assumption.
Aluminum impact factor | Halved (from 19 to 9,5) | Aluminum emission factor is an influent parameter for telecom products. A lower figure depicts a mix of virgin and recycled aluminum supply.
Gold impact factor | Halved (from 49400 to 24700) | Gold has a very high impact that tends to overwhelm the other materials in the result. We try a lower value (like in other databases).
Raw material input factors | Input waste for all raw materials is doubled (an input factor of 1,1 becomes 1,2) | The extra materials needed as input and wasted during production is estimated in the model. We try a more conservative assumption.
IC emission factor | Doubled (from 1,72 to 3,44) | IC is identified in most LCA for ICT studies as a major contributor. In addition, the figure used in the example is rather low compared to other studies.
Assembly emission factor | Doubled | Assembly is very roughly taken into account. We try a more conservative assumption.
Scenario for support operation | A 75% allocation of overall Ericsson operations is assumed instead of 50% | Allocating support operations to a product is challenging. We try a more conservative assumption.
Chart: Climate change potential (ton CO2eq)
| 75% scenario for support operations | Doubling assembly | Doubling IC emission factor | Double the input waste | Halving gold emission factor | Halving aluminum emission factor | Doubling plastics emission factor | Reference
 | 4.5929 | 4.5556 | 4.7334 | 4.6019 | 4.2238 | 4.0797 | 4.4574 | 4.4049

## Slide 14: User review workshop
Is the tool easy to understand without the help of any explanation or documentation?
Participants: approx. 10 within Ericsson
Qualitative feedback after 10 minutes on-boarding experience
Chart: 
| I'm afraid it is going to be too difficult to understand for non knowledgeable users | I'm afraid that the Excel sheet will be too fragile: that the formulas might break and be hard to repair. | I'm afraid that this tool will lead to making carbon footprint claims without all the required scientific rigor. | I'm afraid that the data asked as input will not be easily available for the user. | I would like to fill in an information I have on the product but don't know how to do it.
 | 5 | 2 | 1 | 5 | 2